## Slide 1
GROUP 4 · CSCI 5502 · SPRING 2026
Grid Resilience
& Carbon Analytics
Characterizing Electricity Demand and
Marginal CO₂ Emissions During Hazardous Grid Events
WHY THIS MATTERS
Hazardous grid events — PSPS, extreme heat, equipment failures — force utilities to activate carbon-intensive peakers, spiking marginal CO₂ emissions 15–40%.
This cost is invisible in annual averages. We build the first reproducible pipeline to couple demand and emissions analysis across 52 documented events (2019–2026).
3.5M+
Customers affected
by PSPS (2019–24)
42%
Increase in
grid disruptions
40%
Emissions spike
during events
TEAM
Moulik Kumar · Atharva Zodpe · Pratik Patil
🌐 aazodpe.github.io | github.com/aazodpe/aazodpe.github.io
CORE RESEARCH QUESTION
Can hazardous grid events be automatically characterized by distinct electricity demand
and marginal CO₂ emission profiles using publicly available, high-resolution data?
DATA PIPELINE
📡
WattTime API
5–15 min MOER
(lbs CO₂/MWh)
CAISO region
⚡
EIA-930 API
Hourly electricity
demand (MW)
2019–2026
🚨
Event Catalog
52 hazardous events
PSPS · weather
equipment failures
⚙️
Feature Eng.
Rolling stats · lag
features · deviation
baselines · encoding
APPROACH
01
Baseline construction
Seasonal matching + moving avg + ML-predicted baselines — triangulated for robustness
02
Feature extraction
Peak magnitude · duration · volatility · recovery · coupling coefficients per event
03
Clustering & pattern mining
K-Means archetypes + FP-Growth co-occurrence rules across 1,725 observations
04
Supervised learning
Logistic + Linear regression to quantify predictive signal and demand–MOER decoupling
2.1M
Records post-cleaning
96.8%
Data completeness
52
Validated events
15 features
Per 15-min observation
Data Mining · CSCI 5502 · University of Colorado Boulder · Spring 2026

## Slide 2
CHALLENGES IN DATA COLLECTION, PROCESSING & MODELING
Milestones 2 & 3
DATA COLLECTION & PROCESSING
🔗
Multi-resolution alignment
WattTime at 5–15 min vs. EIA-930 at hourly — demanded resampling, forward-fill, and uniform 15-min UTC indexing across both streams without losing event signal.
❌
Missing & corrupt values
3.2% missing demand, 1.8% missing MOER. Forward-fill for <30 min gaps; linear interpolation for 30 min–2 hr; 142 negative demand values and 28 physically impossible emissions corrected.
📋
No API for hazardous events
Hand-compiled 52 events from CPUC filings, NOAA alerts, utility press releases. PDF extraction + cross-validation against news archives. High labor, irreplaceable for event-level labels.
📊
Baseline construction complexity
Three parallel strategies required — seasonal matching, moving average, and ML-based prediction — to triangulate event impact without attributing normal seasonal variation to events.
MODELING CHALLENGES
🎯
K-Means: limited temporal window
18-day window anchors clusters to single heat-wave episode. Mitigated by weighting hour + is_weekend alongside instantaneous readings.
📉
Logistic Reg: tiny event sample
Only 23 event-level records. 5-fold CV folds have ~5 samples each — accuracy is volatile. ROC-AUC (0.65) prioritized as the stable ranking metric.
📐
Linear Reg: OLS vs. non-linearity
Emergency dispatch breaks the merit-order demand–MOER curve. is_event indicator added iteratively; low R²=0.237 treated as the finding, not a failure.
🌳
FP-Growth: event period too rare
Event windows are only 22.3% of obs (support < 0.30). Event rules present but below top-10 lift. min_support not artificially lowered.
WHAT THESE CHALLENGES REVEALED
⚡ Two granularities, two datasets
15-min time-series (1,725 rows) for clustering & regression; 23-row event-level CSV for classification. Same project, two fundamentally different analytical units.
📉 Low R² = the signal, not noise
OLS explains only 23.7% of MOER — intentionally. Emergency dispatch overrides the normal demand–carbon curve. Richer features (fuel mix, weather) are the Milestone 4 extension.
🔬 Event rarity limits supervised learning
52 events over 7 years → only 23 usable for event-level ML. The small-n constraint drove every pipeline decision: stratified CV, balanced classes, AUC over accuracy.
CODE HIGHLIGHT
# K-Means sweep
for k in range(2, 9):
km = KMeans(
n_clusters=k,
n_init=10)
sil.append(
silhouette_score(
X_sc, labels))
# Best k=4
best_k = range(2,9)[
np.argmax(sil)]
# FP-Growth
freq = fpgrowth(
te_df,
min_support=0.30)
rules = assoc_rules(
freq,
metric='confidence',
min_threshold=0.60)
# Logistic pipeline
pipe = Pipeline([
('imp', SimpleImputer()),
('sc', StandardScaler()),
('clf', LogisticRegression(
class_weight='balanced',
max_iter=1000))])
# CV ROC-AUC = 0.65
cv = StratifiedKFold(5)
cross_validate(pipe,X,y)
Grid Resilience & Carbon Analytics · Group 4

## Slide 3
MODEL RESULTS & KEY LESSONS LEARNED
Milestones 3 & 4
MODEL PERFORMANCE SUMMARY
UNSUPERVISED
K-Means Clustering
Silhouette
0.584
Davies-Bouldin
0.632
4 grid archetypes: High-Stress · High-Emit · High-Demand · Low-Carbon
CLASSIFICATION
Logistic Regression
CV ROC-AUC
0.65
CV F1-Score
0.314
demand_range & duration_hours are strongest predictors of high-emission events
REGRESSION
Linear Regression
R²-Score
0.237
RMSE
105.4
76% of MOER variance unexplained — demand alone cannot represent emergency dispatch
PATTERN MINING
FP-Growth
Max Lift
1.77
Rules
34
off_peak → high_demand rule reveals heat-wave demand shifts normal diurnal patterns
K-MEANS · GRID STATE ARCHETYPES
LOGISTIC REG · ROC CURVE
KEY LESSONS LEARNED
1
Events decouple demand & emissions
R²=0.237 is the finding — emergencies break the normal demand–carbon curve, not a model failure.
2
Duration > peak intensity
Event duration (r=0.84 with total excess CO₂) dominates over peak spike size (r=0.29).
3
API-first pays off
Reproducible, real-time capable pipeline vs. static Kaggle data. Code publicly released.
4
Two granularities needed
15-min time-series for clustering/regression; event-level for classification. Different questions, different units.
CONVERGING FINDING
The low R² of Linear Regression, the modest ROC-AUC of Logistic Regression, and the off_peak → high_demand FP-Growth rule all converge on the same conclusion: hazardous grid events do not simply amplify normal operating patterns — they create fundamentally different demand–carbon dynamics that standard demand-driven models cannot represent.
aazodpe.github.io · github.com/aazodpe/aazodpe.github.io · Group 4 · CU Boulder