## Slide 1
MILESTONE 3 · MODEL IMPLEMENTATION
Moulik Kumar
Atharva Zodpe
Pratik Patil
Group 4 · CU Boulder · April 2026
Grid Resilience
& Carbon
Analytics
Characterizing Electricity Demand and Marginal CO₂
Emissions During Hazardous Grid Events
18 DAYS
Aug 8–25, 2024
1,725
Observations
4
ML Models
15 min
Resolution

## Slide 2
RESEARCH OVERVIEW
“Can hazardous grid events be characterized by distinct electricity demand and marginal CO₂ emission profiles using time-resolved grid data?”
Dataset
WattTime MOER API (5-min emissions)
EIA-930 Demand API (hourly)
CAISO region, Aug 8–25 2024
52,711 raw emission records
Event Studied
Aug 15–18, 2024 CA heat wave
CAISO grid stress + rolling outages
23 catalogued grid events total
384 event rows (22.3% of data)
Four ML Models
K-Means Clustering
Logistic Regression
Linear Regression
FP-Growth Pattern Mining

## Slide 3
DATA PREPARATION FOR MODELS
BEFORE
AFTER TRANSFORMATION
Raw Data Issues
Demand: 75% missing (hourly → 15-min gaps)
Rolling window features had leading NaN values
Season stored as string category
No event labels on time windows
MOER vs. demand magnitude mismatch
Cleaned & Engineered
Demand forward-filled → 0% missing at 15-min
Rolling features back/forward-filled
Season label-encoded; is_peak_hour added
is_event label applied (Aug 15–18 heat wave)
StandardScaler resolves scale mismatch
→
Final Dataset: 1,725 rows × 15 features | Event rows: 384 (22.3%) | Normal rows: 1,341 (77.7%)

## Slide 4
MODEL 1 · K-MEANS CLUSTERING
Why K-Means?
Continuous MOER + demand features match K-Means' Euclidean model. Interpretable centroid-based archetypes without requiring labels — ideal for grid state discovery.
Hyperparameters
k swept 2–8; best k=4 via silhouette score
n_init=20 for stable centroids
StandardScaler applied (MOER vs. demand scale)
4 Grid Archetypes
High-Stress
High-Emit
High-Demand
Low-Carbon
0.584
Silhouette Score ↑
0.632
Davies-Bouldin ↓
4
Optimal Clusters (k)

## Slide 5
MODEL 2 · LOGISTIC REGRESSION (HIGH vs. LOW EMISSION EVENTS)
Why Logistic Regression?
Event-level dataset (23 rows) requires a simple, interpretable model. LR coefficients directly show which demand features drive high CO₂. Replaces RF (rolling features caused data leakage).
Pipeline
Target: high_emission if peak_moer > 60th pct
Features: peak/avg demand, duration, demand_range
SimpleImputer → StandardScaler → LogisticReg
StratifiedKFold CV (5 folds) — honest estimates
Data Source
event_features.csv · 23 event-level rows
AUC=0.65 > 0.5 → demand carries real emission signal
0.48
CV Accuracy
0.31
CV F1-Score
0.65
CV ROC-AUC

## Slide 6
MODEL 3 · LINEAR REGRESSION (DEMAND–MOER BASELINE)
Why Linear Regression?
Establishes quantitative baseline for demand–emissions relationship. Standardized coefficients reveal which predictors drive MOER; residuals expose where linearity breaks down during events.
Key Results
OLS — no regularization (interpretability)
Strongest covariate: hour (std coef = −49.3)
Event term adds +16.9 lbs CO₂/MWh
CAISO solar dip → mid-day MOER valley
Key Insight
R²=0.237 confirms demand alone explains only 24% of MOER variance. Events alter the demand–carbon curve → motivates gradient boosting in Milestone 4.
105.4
RMSE (lbs CO₂/MWh)
11,114
MSE
0.237
R² Score

## Slide 7
MODEL 4 · FP-GROWTH FREQUENT PATTERN MINING
Why FP-Growth?
Discovers co-occurring grid conditions without a predefined target. Prefix-tree is faster than Apriori. Reveals which emission level + demand + time-of-day + event combinations co-occur most.
Hyperparameters
Discretized: MOER/demand (median), time (quartile)
min_support=0.30, min_confidence=0.60
26 frequent itemsets, 34 association rules
Strongest Rule
{off_peak} → {high_demand}
Lift = 1.77 · Conf = 0.88
Event states → high_moer+weekday rules (lift≈1.3)
34
Association Rules
1.77
Max Lift
0.88
Max Confidence

## Slide 8
MODEL COMPARISON & PERFORMANCE SUMMARY
Model | Category | Metrics | Score(s) | Key Insight
K-Means | Clustering | Silhouette / DBI | 0.584 / 0.632 | 4 distinct grid state archetypes discovered
Logistic Reg. | Classification | CV Acc / F1 / AUC | 0.48 / 0.31 / 0.65 | Demand → modest signal; AUC>0.5 confirmed
Linear Reg. | Regression | RMSE / R² | 105.4 / 0.237 | Demand alone explains only 24% of MOER variance
FP-Growth | Freq. Patterns | Max Lift / Rules | 1.77 / 34 rules | Off-peak ↔ high-demand association (CAISO pattern)
★ LR AUC=0.65 on just 23 events confirms demand-side features carry real predictive signal for emission-level classification.

## Slide 9
KEY FINDINGS
01
4 Distinct Grid States
K-Means reveals High-Stress, High-Emit, High-Demand, and Low-Carbon archetypes. Low-Carbon cluster has 36% event overlap — the CAISO heat wave drove a renewable surge despite record demand.
02
Demand Signals Emissions
Logistic Regression (CV AUC=0.65, 23 events) confirms demand-side features carry real predictive signal for high-emission events. Demand range and event duration are the strongest coefficients.
03
Non-Linear Dynamics Dominate
Linear Regression R²=0.237 validates that demand alone explains only 24% of MOER variance. Event residuals show systematic over-prediction, proving hazardous events alter the demand–carbon curve.
04
Off-Peak ↔ High Demand Pattern
FP-Growth: {off_peak} → {high_demand} (lift=1.77, conf=0.88) reflects CAISO’s overnight industrial load. Event states link to high_moer+weekday combinations (lift≈1.3), consistent across clustering and FPM.

## Slide 10
LIMITATIONS & FUTURE WORK (MILESTONE 4 ROADMAP)
LIMITATIONS
MILESTONE 4 ROADMAP
18-Day Window
Only one heat-wave event observed. Full 2019–2026 coverage pending WattTime API expansion.
Small Event Sample
23 events limits classification power. More events needed for stable CV.
Linear Baseline Only
OLS cannot capture non-linear event–demand–MOER dynamics.
Discretization Sensitivity
FP-Growth rules depend on binning choices; median-split partially mitigates this.
TimeSeriesSplit CV
Apply proper time-series cross-validation for honest out-of-sample evaluation.
XGBoost / LightGBM
Replace linear regression with gradient boosting for non-linear event dynamics.
Expand Event Coverage
Include PSPS and winter demand spikes across CAISO, PSCO, ERCOT regions.
SHAP Explainability
Add SHAP values to quantify per-feature contributions at event level.

## Slide 11
CONCLUSION
Hazardous grid events leave measurable, distinct,
and detectable signatures on the electricity
grid’s carbon intensity profile.
K-Means
Silhouette 0.584
Logistic Reg.
AUC 0.65
Linear Reg.
R² 0.237
FP-Growth
Lift 1.77
Thank You
Moulik Kumar · Atharva Zodpe · Pratik Patil
Group 4 · Data Mining · University of Colorado Boulder · April 2026